## Slide 1
NOAA Satellite Science Week
William Denig
Solar & Terrestrial Physics Division
NOAA/NESDIS/NGDC
303 497-6323
William.Denig@noaa.gov
GOES-R Space Weather
Operations to Research (O2R)

## Slide 2
GOES-R Space Weather (SWx)
Maintaining a Long-term Record of Space Weather

## Slide 3
GOES-R Space Weather (SWx)
GOES-R Sensors Supporting O2R
GOES-R includes of a complement of in-situ particle/field and solar-viewing sensors providing a synoptic assessment of space weather.
SENSOR
Space Environmental In-Situ Suite (SEISS)
Solar Ultra-violet Imager (SUVI)
EUV and X-Ray Irradiance Sensors (EXIS)
Magnetometer (MAG)
IMPROVEMENT
Improved energy range / contamination rejection
Multi-wavelength solar imagery
Improved accuracy and precision
Gradiometer rejection of satellite generated fields
SCIENCE APPLICATION
Spacecraft charge models for electrostatic discharge
Surface features and thermal height profiles
Solar backgrounds/events impacting climate models
Geomagnetic field data with improved fidelity
SEISS
SUVI
EXIS
MAG

## Slide 4
GOES-R Space Weather (SWx)
Why So Many Sensors?
This is what you see!

## Slide 5
GOES-R Space Weather (SWx)
Why So Many Sensors?
This is what we see!

## Slide 6
GOES-R Space Weather (SWx)
Protecting Space Assets – GEO is a Busy Place

## Slide 7
GOES-R Space Weather (SWx)
New Datasets for Spacecraft Charge Modeling
SEISS provides an improved in-site assessment of the local spacecraft charging environment.
Extended low energy range for modeling surface charging
Extended mass range for monitoring penetrating radiation
Example: Galaxy-15
Anomaly: 05 April 2010
Internal Charging/ESD
NGDC Report
Example: SkyTerra-1
Anomaly: 07 March 2012
Single-Event Upset
NGDC Report
GOES-R will provide new data to better serve the satellite charge modeling community
Reference: Ferguson, D.C., W.F. Denig and J.V. Rodriguez (2011), Plasma Conditions During the Galaxy 15 Anomaly and the Possibility of ESD from Subsurface Charging, 49th AIAA Aerospace Sciences Meeting, 04-07 Jan 2011, Orlando FL.

## Slide 8
GOES-R Space Weather (SWx)
Cataloging Satellite Anomalies – Future Mission?
Reference: Denig, W.F., R.J. Redmon, J.V. Rodriguez and J.H. Allen (2014), Book Review: Satellite Anomalies: Benefits of a Centralized Anomaly Database and Methods for Securely Sharing Information Among Satellite Operators, Space Weather, 12, 528–529, doi:10.1002/2014SW001100.
Link

## Slide 9
GOES-R Space Weather (SWx)
Monitoring the Occurrence of Solar Storms
-150
18:00
21:00
UT
250
0
Hp
GOES-15
RE
During stronger space weather events the magnetopause location moves inside of the geostationary orbit.
At these time, satellites on the dayside are exposed to the interplanetary plasma conditions.
Sun
Algorithm development supported by GOES-R Risk Reduction (GOES-RRR)
Implementation support by the Satellite Product & Services Review Board (SPSRB) – Link

## Slide 10
WAAS Coverage 27 February
TEC 27 February 22:30 UT
NGDC Magnetopause Crossing
27 Feb 14 – 17-24 UT
FAA Message to SWPC: “An Ionospheric Storm began on 2/27/14. The Satellite Operations Specialists were alerted at the WAAS O&M by a Significant Event 757 at 2120 Zulu. So far, LPV and LPV200 service has not been available in Eastern Alaska and Northeastern CONUS. At times, North Central CONUS and all of Alaska have lost LPV and LPV200 Service.”
Storm Day
Magnetopause Standoff Distance
27 Feb 14
GEO
WAAS Coverage 26 February
TEC 26 February 20:45 UT
Reference Day
GOES Magnetic Field
Magnetopause
Location
27 Feb 14
19:58 UT
LPV - Lateral Precision with Vertical guidance
GOES 15
GOES 14
GOES 13
GOES-R Space Weather (SWx)
Monitoring the Performance of WAAS

## Slide 11
>0.8 MeV electron flux in equatorial plane in SM coordinates.
Rebuilding of Earth’s outer radiation belt during 8-9 October 2012 geomagnetic storm
GOES-15
and RBSP-A
spacecraft
positions
[After Kress et al., GRL, 2014]
Kress, B. T., M. K. Hudson, and J. Paral (2014), Rebuilding of the Earth's outer electron belt during 8–10 October 2012, Geophys. Res. Lett., 41, 749–754, doi:10.1002/2013GL058588.
GOES-R Space Weather (SWx)
Repopulating the Magnetosphere

## Slide 12
SDO AIA solar images are used as proxy for SUVI. SUVI Thematic Maps (SUVI.19) and Coronal Hole Boundaries (SUVI.15) are L2+ SWx products.
CH Shape File
Thematic Map
Finite Vertices
Coronal Hole Boundary
NASA/SDO as Proxy
9/18/2012 20:29:01
Coronal holes are regions of the corona where the magnetic field reaches out into space rather than looping back down onto the surface. Particles moving along those magnetic fields can leave the sun rather than being trapped near the surface. Recurring larger solar speeds originate within coronal holes.
GOES-R Space Weather (SWx)
SUVI Classification of Solar Coronal Holes (CH)

## Slide 13
Classification | All flares | Good backgrounds
X-class flares | 3.0±1.7 arcminutes | 3.0±1.6 arcminutes
M-class flares | 4.0±3.4 arcminutes | 3.7±3.2 arcminutes
C-class flares | 7.3±6.1 arcminutes | 6.7±5.6 arcminutes
Initial PLPT performance results using “quad-diode” proxy data from SXI compared to the NOAA flare catalog (5 arcminute requirement).
New quad-diode in XRS will provide solar flare locations
GOES-R Space Weather (SWx)
Exploiting New Capabilities for the EXIS/XRS

## Slide 14
Funded as a University of Colorado/CIRES Innovative Research Project.
GOES-R Space Weather (SWx)
EUVS Continuous Monitoring of the Geocorona
Background: Use occultation technique to monitor the hydrogen geocorona at 121.6 nm (Lyman alpha) within the upper thermosphere. Atomic hydrogen in this region is a byproduct of hydrogen-containing species below such as methane and water vapor. Models have predicted 50-75% increases in upper atmospheric hydrogen as a consequence of a doubling of tropospheric concentrations of methane, a primary greenhouse gas.
GOES-R data will allow for establishment/continuation of a long-term (since 2006) record.
Notes: American Geophysical Union, Spring Meeting 2007, abstract #SA53A-04
Abstract: Ground-based Fabry-Perot observations of the hydrogen Balmer-alpha emission have been used since the late 1970s to investigate hydrogen in the geocorona, spanning the upper thermosphere and exosphere. Atomic hydrogen in this region is a byproduct of hydrogen-containing species below such as methane and water vapor. Models have predicted 50-75 % increases in upper atmospheric hydrogen as a consequence of a doubling of tropospheric concentrations of methane, a primary greenhouse gas. The 11-year solar cycle is a dominant source of natural variability in the upper atmosphere and its effect on hydrogen distributions and emissions must be understood to investigate possible signs of longer-term climatic trends. We will discuss data from the present near-solar minimum winter compared with those from the previous near- solar minimum period of 1997, all taken with the same instrument, the Wisconsin H-alpha Mapper Fabry-Perot (Kitt Peak, AZ), and using the same nebular calibration source for absolute intensity calibration. The newer data are consistent with observations over the rise of the solar cycle with lower intensities observed during solar minimum compared with solar maximum conditions. We will also discuss preliminary comparisons with earlier data and the extra challenges associated with comparing data taken with different, though similarly designed instruments. The geocoronal hydrogen column emission observed by the Fabry-Perot is a function of the hydrogen density profile, the solar excitation flux, and radiative transfer including the contribution of multiple scattering below the Earth's shadow. We will discuss work in progress to use forward modeling to retrieve the hydrogen column abundance from the emission observations.

## Slide 15
GOES-R Space Weather (SWx)
Parting Thoughts – Bill Denig
While the primary mission of GOES space environment sensors is to serve the needs of operational space weather community the data, nevertheless, contributes significantly to heliophysics (and related) research:
Over 40 years of continuous space environmental data
  SMS1&2 (7/74 – 4/76) /// GOES 1-15 (1/76 – present)
GOES extensively used in peer-reviewed publications
  75 of 711 papers published in JGR-Blue in 2013
Data available via NGDC (main site) and other sources
  NGDC: http://www.ngdc.noaa.gov/stp/satellite/goes/
  NASA CDA-Web: http://cdaweb.gsfc.nasa.gov/
  VIRBO: http://virbo.org/